## Slide 1
Raytheon Missile System Interchangeable Virtual Instrumentation
Solution From 2004 to 2012
Hugh Smith and Fred Wiegand

## Slide 2: Introduction
  The IVI standard presented features to “Reduce the Cost of Test”
  Supports instrument interchangeability and addresses instrument obsolescence
  Reliable and centralized configuration store for driver and test
In 2006 Presented Autotestcon summary of current deployments
  Standards for vendor drivers add consistency
  Reliable centralized configuration store for driver and test station setup
  Created classes and drivers for instruments not defined by IVI Foundation
Evolution of IVI Based Test Software Architecture
  Migrating to new development environments
    Successful rebuilds in new operating systems and Visual Studio versions
    New roadmap in ATEasy development environment
  Addition of IVI-COM and LXI

## Slide 3: Software Architecture 2006
The Software Architecture Using IVI Technology

## Slide 4: Getting Started with IVI and Creating New classes
IVI-C development
NI Measurement & Automation Explorer (NI MAX) selected for configuring Test Systems
  Tools for station setup and troubleshooting
  Took advantage of Simulation mode
Project needs an instrument not addressed by the IVI Foundation
  No existing API spec
  No existing IVI Class driver
  Created Specification Document developed using UML
    Assign an engineer familiar with the Instrument
    The Specification is reviewed by a group of engineers
    The Specification document becomes the design instructions for the API, IVI Class Driver and IVI Instrument Specific Driver

## Slide 5: Creating New Instrument Classes and Drivers
Focused on creating IVI-C Classes and Instrument Drivers
  Created Visual Studio wizards
    Wizard set expanded to middleware, drivers and test apps
    “1 development environment” makes integration and debug easier
    Calling conventions and exports more consistent with middleware and Raytheon test executive
Create the most commonly used inherent functions
  Init and Close all drivers the same way
  Consistent approach to error handling and creating error messages
IVI-C drivers support the “80% solution” in API specs
  Drivers for IVI defined classes are tailored down to “just what they need to be”
    No requirement to support users outside of Raytheon test equipment
  Instrument specific attributes defined for a new class
  Drivers work with IVI Engine to support “State Caching”, “Range Checking” and “Simulation

## Slide 6: Creating New Instrument Classes and Drivers
Whenever possible wrapping PNP drivers and vendor libraries
  Already have a low level API for instrument control
    No learning curve on command formats
    Message formatting and timing requirements addressed
  Most include range checking for input parameters
  Most include error handling and meaningful instrument specific error messages
Created a VISA interface
  Most instruments controlled by VISA library
    Main exception is PCI based instruments
  All commands in VISA spec brought out through middleware
  Used for test apps that cannot wait for upgrades to APIs and Drivers

## Slide 7: 2006 RMS IVI Classes
Incorporating the 8 IVI Foundation Classes
  DC Power, DMM, Function Generator, Oscilloscope, Power Meter, Spectrum Analyzer, Switch, RF Signal Generator
    Supporting 21 Instrument drivers
Creating 18 COTS Classes
  1553, Ac Power , Comparator, counter, DAC, Digitizer, DIO, Electronic load, IEEE 1394 Firewire, IR Target, Jtag, Motion Control, MpDio, Phase generator, Switch Exec, Telemetry System, Trap, TSAT Visa
    Supporting 23 Instrument drivers
    Created an interface to National Instruments Switch Executive
    Created an interface to communicate with Instruments using VISA command
Inventing 10 Special UUT Interface Classes
  RMS CAE, Active Target, RF Link1, RF Link2, Gas Chassis, Control Panel, IRU, Target Coupler, Launcher Message, Power sequence

## Slide 8: Results at 2006
The System Software with IVI technology
  Used across ten product lines
  Deployed on over twenty test systems
  Production and engineering test systems
  Testing hardware from circuit cards to all up rounds
  Using test products from 28 different companies
IVI Technology provided the ability to swap hardware without changing test software
  Test Team was able to swap an Agilent 66xx series power supply with a N6700 series power supply
  Download an IVI driver from National Instruments web site
  Make the updates with MAX to reconfigure the system with the new power supply
  And had the system operational before lunch that day

## Slide 9: IVI at RMS Since 2006
Maintenance and Growth of the Product
  New classes and support
Changing OS and the development environment
  Windows and Visual studio
Migrating the IVI architecture
  Taking advantage of ATEasy architecture
  New interface development
  Adding IVI COM
LXI and the IVI solution
  Easy
  GUI interface to Trouble shoot
Configuration Tools
  Valuable asset

## Slide 10: Growth, Maintenance and Support
Limited New IVI Class develop since 2006
  COTS and RMS specific
    Temp and Vibe
    Utilities – Calibration tables
    Product line special interfaces
System Software Product with IVI technology
  2004 to 2006 Development and deployment as a software product
    8 to 10 engineers to develop and integrate
  2007 to 2009 Continued deployment and support
    3 to 5 engineers to support and upgrade
  2010 to 2012 Software product maintenance
    1 to 2 engineers to maintain and support product lines
Installation as Software Product
  Product lines take ownership and use IVI architecture
  Mods rolled back into software product maintenance

## Slide 11: IVI Evolution with Windows and Development Environments
Windows
  Windows 2000 to Windows XP to Windows 7
  Issues with registry usage when moving beyond Windows XP resolved with move to INI files
  Support for manifests attached to applications
  Tools for CM reworked moving from 32 bit to 64 bit operating systems
Changes to Microsoft Visual studio
  Visual Studio 2003 to 2005 to 2008
  Minor code changes
  Support for manifests from Visual Studio 2008
  Regression testing with Visual Studio 2010 but not a full conversion of project files

## Slide 12: ATEasy Architecture Talking Points
ATEasy development environment that makes separation of Program and System software more intuitive
  Use the IVI Configuration Store and NI Switch Executive to standardize configurations
  Replace complexity of Middleware and Class Drivers with "command" interface of ATEasy drivers
  Create interchangeability in "command" interface of ATEasy drivers
  Make ATEasy drivers similar and simplify maintenance by wrapping Agilent IVI-COM drivers
  IVI-COM eliminates "DLL Hell" by registering components

## Slide 13: New Interface Development
Most new driver development in the ATEasy Architecture
  IVI drivers preferred for consistency but not a requirement
  Interchangeability at the ATEasy driver “command” level
RF Instrument suites built upon IVI-COM drivers
  Adds consistency in ATEasy drivers by using vendor drivers
  Some custom interfaces pass through commands
High speed serial and custom serial protocols built upon vendor drivers that integrate into the IVI Configuration store
  Built upon firmware solutions in FPGAs
  Becomes a virtual instrument depending upon firmware load
  Vendors provide IVI drivers for firmware reads and writes

## Slide 14: IVI and the LXI interface
LXI drivers come with an IVI driver and web interface
IVI driver can be integrated into higher level software architectures
Additional LXI benefits
  Web based interface very helpful in instrument setup and quick start without test software
    Basic troubleshooting when nothing else is working
    No software to maintain for running a soft front panel
  Integration feedback on LXI advantages
    No GPIB or VXI configurations required
      No dip switches to set
      No COM ports that renumber themselves
    Eliminates problems with proprietary V16/V24/V32 address spaces
      Recent issues using VME cards in VXI chassis

## Slide 15: Configuration Tools
NI-MAX is the configuration tool of choice
  User interface for working with “IVI Drivers” in IVI Configuration Store
  User familiarity from previous deployments
  User interface for NI Switch Executive
  Troubleshooting directly with instruments and passing commands through to message based and register based instruments
A few specific requirement to use Agilent Connection Expert
  Setup for LXI slot 0 VXI controller
  Setup for USB to GPIB controller
  Requirement to be installed for some Agilent IVI-COM drivers

## Slide 16: Conclusion
  First option for all RMS test systems
The RMS Test Software with IVI technology
  Production and engineering test systems
  Tests hardware from circuit cards to all up rounds
  Supports multiple development environments
  Adapt test instrumentation from any company
  Used on the majority of RMS product lines
RMS Test Software compatible with countless IVI drivers that are available on the Internet